## Slide 1: Introduction to Arduino and Arduino Programming
ASTM 1613
Fundamentals of Agricultural Systems Technology

## Slide 2: Objectives
Upon completion of this lesson, you should be able to:
  Explain what an Arduino is;
  Identify the primary components of the Arduino UNO and explain the basic function(s) of each component;
  Explain the use and internal wiring of a breadboard;
  Identify and explain the use of resistors and light-emitting diodes (LEDs);
  Understand the basic structure of the Arduino Integrated Development Environment (IDE);
  Breadboard a simple electronic circuit and write an Arduino sketch (program); and
  Verify/Compile/Debug the Arduino Sketch and upload it to the Arduino UNO.

## Slide 3: Outline
Arduino UNO
  What is it and what are its primary components?
Breadboards
  What are they and how do you use them?
Resistors and Light Emitting Diodes (LEDs)
  What are they and how are they used?
Programming an Arduino UNO
  How do I write, compile, and upload a “sketch” using the Arduino Integrated Development Environment (IDE)?

## Slide 4: What is an Arduino?
An Arduino is a programmable microcontroller
  Programmable = receives and executes user programs
  Micro = small
  Controller = Controls other electronic/electrical components
A microcontroller consists of:
  A microprocessor unit (MPU)
  Memory
  Peripherals
Widely used in LOTS of applications
  Some tractors contain dozens of on-board microcontrollers!
The Arduino UNO is a specific model of Arduino
Enlarged 4 X
Arduino UNO

## Slide 5: Primary Components of the Arduino UNO
ATMEGA328P – is the microprocessor – the “brains” of the microcontroller
Header(s) – Contain identified or numbered pins connections
  Power pins
    3.3 V
    5 V
    Ground (GND) – 3 total GNG pins
  Digital (LOW/HIGH signals)
    Digital pins are either HIGH (5 V) or LOW (0 V)
    All digital pins can all be configured as either:
      lNPUT - receives information from a sensor connected to the pin and sends it to the microprocessor
      OUTPUT - receives information from the microprocessor and sends to a device connected to the pin
USB port – Connects the Arduino to a computer for programming and for power. Connects with a USB Type 2 cable (not shown)

## Slide 6: Breadboards, Resistors, LEDs, and Pin Connector Wires

## Slide 7: Breadboards
A breadboard is a device for constructing electronic circuits without soldering components
  Components and wires are inserted into the electrically connected breadboard holes to build circuits

## Slide 8: Resistors
Widely used in electronic circuits to:
  Limit voltage/current to a “safe” level
    Rated in Ohms (𝛺)
    Bend the resistor’s “legs” to insert in slots on breadboard

## Slide 9: Light-Emitting Diodes (LEDs)
A semiconductor component that emits light (photons) when current flows through it
  Widely used as indicator lights
Forward-biased LED
Anode
Cathode
  LEDs will only conduct when “forward-biased”

## Slide 10: Connecting the Arduino UNO to the Breadboard with “Pin Connector” Wires
Pin Connector Wire
Pin connector wires connecting Digital pin 3 and GND to breadboard

## Slide 11: Breadboarded LED/Resistor Circuit Controlled by the Arduino UNO
The 240 𝛺 resistor and the LED are wired in series between digital pin #3 and GRD (ground)
Digital pin #3 is configured as an OUTPUT
Whenever the Arduino sketch causes Digital pin #3 to go HIGH (+5V) the LED will light up
Whenever the Arduino sketch causes Digital pin #3 to go LOW (0V), the LED will NOT light up

## Slide 12: Why Do We Need a Resistor in this Circuit?
The Arduino UNO has an output voltage of 5 volts
Each digital output pin has a maximum output current of 0.020 amps (continuous)
A typical LED has an approximate resistance of 15 𝛺
  Amps =
So, we add a 240 𝛺 resistor in series with the LED
  Amps =
The resistor limits current to a safe level
Resistor

## Slide 13: The Arduino Integrated Development Environment (IDE)
Is a “text-based” programming environment
An Arduino sketch program contains two primary functions:
  void setup
    The setup function is called once when your program starts
      Used to initialize pin modes (INPUT or OUTPUT)
  void loop
    The loop function runs in a continuous “loop”
      Contains the instructions the Arduino executes as long as the board is powered
File  New

## Slide 14: Common Arduino Programming Functions
Used in the void setup function
  pinMode
    Specifies a specific pin to be either an OUTPUT or an INPUT
      Generic form:
        pinMode(pin_number, OUTPUT or INPUT);
      Specific form:
        pinMode(3, OUTPUT);
          specifies that pin #3 on the Arduino UNO will be used as an output
Used in the void loop function
  digitalWrite
    Outputs either HIGH or LOW (turns On or turns Off) the specified digital pin
      Generic form:
        digitalWrite(pin_number, HIGH or LOW);
      Specific form:
        digitalWrite(3, HIGH);
          Outputs HIGH to pin #3 (turns On whatever device is attached to pin #3)
  delay
    Causes the program to wait a specified amount of time before proceeding to the next command.
      Generic form:
        delay(ms);
      Specific form:
        delay(1000);
          Causes the program to wait 1000 milliseconds (1 second) before proceeding to the next command
Note: There are many other functions, but these are the three we will need for our sample program and activity.

## Slide 15: A Simple Arduino Sketch to Make the LED Blink
Declares pin 3 as an output
because pin 3 is a digital pin, it is a digital output
Causes pin 3 to output a “HIGH” value (+5 V)
Causes program to delay for 1000 milliseconds
Causes pin 3 to output a “LOW” value (0 V)
Causes program to delay for 1000 milliseconds
Note the specific syntax required for:
  pinMode(3, OUTPUT);
  digitalWrite(HIGH or LOW);
  Delay(1000);
Note that each program statement ends with a semi-colon  ;

## Slide 16: Summary
The Arduino UNO is a microprocessor
  It is programmable and can receive inputs and send outputs
  Microprocessors are widely used in agriculture and industry
The Arduino UNO contains
  Power pins
  Digital pins
  Analog pins
We can build and connect temporary electronic circuits containing resistors, LEDs and other components to the Arduino UNO using pin connectors
Arduino UNO programs are called “sketches”
  A sketch consists of two primary functions:
    Void Setup
      pinMode
    Void Loop
      digitalWrite
      delay
  You can use “comments” to document your sketch

## Slide 17: Adding “Comments” to Document Your Sketch
Comments are for your use in documenting your sketch
The IDE ignores comments when it runs
To write a short comment, start with two forward slashes:
  //the program will ignore text to end of line
To write a longer comment, start with a forward slash and asterisk and end with an asterisk and a forward slash:
/*the program will ignore everything in between*/

## Slide 18: Uploading Your Sketch to the Arduino UNO
Note: The Arduino UNO must be connected to the computer using the USB Type 2 cable in order to upload a program.

## Slide 19: Looking Ahead  Activity Circuit
[Video in actual lesson]